## Slide 1: 24-783 Lecture 18

## Slide 2
Polygonal Mesh Data Structure
Finding Connected Vertices
Finding Neighboring Polygons
Introducing YsShellExt class
Color-map problem
Greedy-Search Path Finding
Flood-Fill in a Polygonal Mesh

## Slide 3: Finding Connected Vertices
Using vertex-to-polygon table, we want to find connected vertices.
Add a function called: std::vector <VertexHandle> GetConnectedVertex(VertexHandle fromVtHd) const;

## Slide 4: Finding polygons from an edge.
Want to find polygons from a pair of vertices. std::vector <PolygonalMesh::PolygonHandle> PolygonalMesh::FindPolygonFromEdgePiece( VertexHandle edVtHd0,VertexHandle edVtHd1) const
Also want to find a neighboring polygon of a polygon. PolygonHandle GetNeighborPolygon(PolygonHandle plHd,int n) const;

## Slide 5: Drawing a connectivity graph (Dual)
Connectivity graph of dual: A graph constructed by connecting the centers of the neighboring elements.
If the triangulation is a Delaunay triangulation, this is called a Voronoi diagram.

## Slide 6
Starting from the picking example.
D-key : Show dual
N-key : Back to the normal view

## Slide 7: Depth-first and breadth-first search in binary tree
Depth-first search
  Normal traversal of a binary tree.
Breadth-first search
  Visit higher-nodes first.

## Slide 8: Implementation
Depth-First search: LIFO (Last-In First-Out) buffer
  Stack is a LIFO buffer.
  That’s why depth-first search can easily be implemented with a recursion.
Breadth-First search: FIFO (First-In First-Out) buffer
  Queue. Can be implemented with a linked-list.
  Can also be done by a doubling-array.

## Slide 9: Breadth-First Search in a Graph
Finding N-neighbors
0
1
1
1
2
2
2
2
2
2
3
3
3
3
3
3
3
3
3

## Slide 10: Breadth-First Search in a Graph
Need to prevent back fire.
Unlike a tree, there is a path to come back to a node that has already visited.
Without keeping track of the already-visited nodes, it falls into an infinite loop in the worst case.
0
1
1
1
2
2
2
2
2
2
3
3
3
3
3
3
3
3
3

## Slide 11: Breadth-First Search in a Graph
Use a hash table for preventing infinite recursion.
Make a hash table that connects a node (in this case, a polygon) and the depth.
When exploring a new node, check if the node is already in the hash table.
  If it is included, the node has already been visited and does not have to re-visit.
  If it is not, the node should be visited next.

## Slide 12: Selecting edge-connected vertices within certain radius from a picked vertex.
Can be depth-first or breadth-first search.
Needs same mechanism to stop back fire.
Example: Highlighting vertices within 2.0 radius of the clicked vertex.

## Slide 13: Highlighting High Dihedral-Angle Edges
Dihedral angle
An angle between two neighboring polygons.
Give a clue of feature edges.
Identifying high dihedral-angle edges is important for feature identification.

## Slide 14: Greedy Path Finding
Let's find a path between two picked vertices with the greedy-search.
You can use YsShellExt::GetConnectedVertex and step to the one that is closest to the goal.

## Slide 15: Introducing YsShellExt class
I hope you know how you can write a polygonal mesh data structure by now.
Let's use YsShellExt class from now on.
YsShellExt class has all functions (except MergeVertex) that PolygonalMesh class has.
Plus constraint-edges, face-groups, and utility libraries.
Same function name, same parameter. You can pretty much replace PolygonalMesh class with YsShellExt.

## Slide 16: Using YsShellExt class
Add geblkernel in target_link_libraries instead of polygonalmesh.
Add #include <ysshellext.h> instead of polygonalmesh.h
Replace PolygonalMesh with YsShellExt.

## Slide 17: Identifying a mesh type
YsShellExt class is independent of OpenGL (only depends on C++11 standard)
Can be used for building a command-line program.
Example: Identifying a mesh type.

## Slide 18: Re-writing the Picking (and other features) Program with YsShellExt

## Slide 19: Color-map problem
4-color theorem: You only need four colors to paint all polygons so that no neighboring polygons have the same color.
It is true for any genus-0 geometry.
Obvious for a triangular mesh.
If you don’t care about the minimum number of triangles, it is not a big deal.
You can easily implement it if you know neighboring polygons.

## Slide 20
std::vector <YsColor> palette;
palette.push_back(YsBlue());
palette.push_back(YsRed());
palette.push_back(YsGreen());
palette.push_back(YsYellow());
palette.push_back(YsMagenta());
palette.push_back(YsCyan());
palette.push_back(YsDarkBlue());
palette.push_back(YsDarkRed());
palette.push_back(YsDarkGreen());
palette.push_back(YsDarkYellow());
palette.push_back(YsDarkMagenta());
palette.push_back(YsDarkCyan());
for(auto plHd : shl.AllPolygon())
{
std::vector <bool> used;
used.resize(palette.size());
auto nEdge=shl.GetPolygonNumVertex(plHd);
for(decltype(nEdge) i=0; i<nEdge; ++i)
{
auto neiPlHd=shl.GetNeighborPolygon(plHd,i);
if(nullptr!=neiPlHd)
{
auto neiCol=shl.GetColor(neiPlHd);
for(int j=0; j<palette.size(); ++j)
{
if(neiCol==palette[j])
{
used[j]=true;
break;
}
}
}
}
int unusedIndex=-1;
for(int k=0; k<palette.size(); ++k)
{
if(true!=used[k])
{
unusedIndex=k;
break;
}
}
if(0<=unusedIndex)
{
shl.SetPolygonColor(plHd,palette[unusedIndex]);
}
else
{
// You come up with a new color,
// use it, and add to palette.
}
}

## Slide 21: Greedy-Search Path Finding
Starting from a vertex, find a neighboring vertex that shortens the distance to the goal the most.
Repeat it until reaching the goal or no more next vertex is found.

## Slide 22
std::vector <YsShell::VertexHandle> FindPath(
const YsShellExt &shl,
YsShell::VertexHandle fromVtHd,YsShell::VertexHandle toVtHd) const
{
double dist=shl.GetEdgeLength(fromVtHd,toVtHd);
std::vector <YsShell::VertexHandle> path;
path.push_back(fromVtHd);
auto vtHd=fromVtHd;
while(vtHd!=toVtHd)
{
double bestDist=dist;
YsShell::VertexHandle nextVtHd=nullptr;
for(auto vtHdCandidate : shl.GetConnectedVertex(vtHd))
{
double candidateDist=shl.GetEdgeLength(vtHdCandidate,toVtHd);
if(candidateDist<bestDist)
{
nextVtHd=vtHdCandidate;
bestDist=candidateDist;
}
}
if(nullptr==nextVtHd) // Failed.
{
path.clear();
return path;
}
path.push_back(nextVtHd);
vtHd=nextVtHd;
dist=bestDist;
}
return path;
}

## Slide 23: Flood Fill in a Mesh
Recall 2D version.

## Slide 24: Flood Fill
Start from one pixel and fill all the connected pixels that has same color.

## Slide 25: Flood Fill
First step: Paint the first pixel

## Slide 26: Flood Fill
Then look at all the pixels around the first pixel that has the source color.

## Slide 27: Flood Fill
Then repeat it until you have no more pixel to look at.

## Slide 28: Flood Fill in a Mesh
In 3D, you start from a polygon and walk onto the neighboring polygons.